3GPP TSG SA WG2 Meeting #136	S2-1911794

Nov 18 – 22, 2019, Reno, NV

Source:	InterDigital Inc., ITRI

Title:	New key issue on deployment consideration to enable seamless change of EC Application Server, serving UEs

Document for:	Approval

Agenda Item:	8.5

Work Item / Release:	FS_enh_EC/Rel-17

Abstract: This paper proposes a key issue to study deployment consideration to enables seamless change of application server serving the UE.

# 1	Proposal

The objectives of FS_enh_EC (in SP-190185) include “Improvements to 5GC support for seamless change of application server serving the UE”. It is also noted that the study will not consider application layer solutions.

It is proposed to add a key issue to study deployment consideration to enables seamless change of application server, evaluating deployments aspects of a 5GC based or Application Layer based solution.

**** First change *****

## 5	Key Issues

## 5.X	Key Issue #X: 5GC deployment considerations to enable seamless change of EC Application Server

## 5.X.1	General description

Application instances running on an edge application server may be passthrough or may terminate a data session with the UE. In addition, applications instances running on an Edge Application Server can also be stateful or stateless.

Seamless change of the Application Server for a terminating application instance may be enabled either using an application layer mechanism, or through a mechanism provided through the 5GC.

This Key Issue addresses the following items:

- Taking into consideration the output of TR 23.758, evaluate and determine what type of mechanisms for seamless change of Application Server should be enabled and how:

  - Study whether Application layer mechanism or 5GC mechanisms should be employed to address seamless change of Applications Servers serving the UE

Note: Application Layer solution are out of scope of SA2. The study is not expected to address application layer solutions just determine whether an application layers solution or a 5GC solution is preferred

- Taking into consideration the output of TR 23.758, evaluate and determine whether and how seamless change of Application Server can be enabled considering:

  - Application servers in 5GC, in third party networks, or both

  - Passthrough applications, Terminating Data Session applications or both

  - Stateful and Stateless applications

**** End of change *****